Coversheet

The Coversheet has to contain the following:

- Heading “Electrical Safety Form CSC2016”

- University and Team Name

- Snowmobile number

- Main Team Contact for ESF related questions

Feel free to add team logo, snowmobile picture, and the like.

Requirements (delete this section after you have read and understood it):

Maximum number of pages for the complete ESF is 100 pages!

Links to video or audio data are prohibited.

If you did not fill out the tables or if you changed the format of the ESF Template, you will fail by default.

Every single part/heading of the ESF Template must be filled with content. If the respective part is not relevant for your concept, describe shortly why not.

The respective parts of the ESF template provide guidance on the type of information which should be included in each section or the rules which should be addressed by the section.

The table of contents must be hyperlinked.

The generated PDF must contain hyperlinked bookmarks (an example can be found in the CSC2016 rules for example).

Use internal reference links. For example when describing wiring and mentioning a figure in the text then link it to the figure.

Do not just copy all of your datasheets in the appendix, e.g. we do not need to know what you have to do to program your motor controller; we do not need the whole user manuals of microcontrollers to review your ESF, etc.

Single pages/figures/tables extracted from the complete datasheet showing the important parameters, figures, etc. are usually sufficient, but the source/link to the complete datasheet has to be provided. If the datasheet describes more than one type, clearly mark in the datasheet to which type you are referring / which type you plan to use.

Datasheets should only be used as a reference. Please cover the important data in your text by using tables, figures, etc.

If you refer to parts of a data sheet, then you need to provide an internal document links from the text to the respective datasheet and another internal document link back from the datasheet to the text section.

For example a link in the motor controller section “The datasheet can be found here (clickable)” and a link above the motor controller datasheet in the appendix “The section covering the motor controller can be found here (clickable)”.

If you do not include the appropriate portions of datasheets in the appendix or include appropriate internal document links you will fail by default.

If you are unsure with respect to feedback of the reviewer, do not hesitate to write an e-mail and ask.

Parts of the ESF which are changed because of reviewer’s feedback have to be marked in red.

Following these guidelines will guarantee a swift review process.

Table of Contents

Table of Contents	ii

I	List of Figures	v

II	List of Tables	vi

III	List of Abbreviations	vii

1	System Overview	1

2	Safety Systems	2

2.1	Shutdown Circuit	2

2.1.1	Description/concept	2

2.1.2	Wiring / additional circuitry	2

2.1.3	Position in snowmobile	3

2.2	IMD	3

2.2.1	Description (type, operation parameters)	3

2.2.2	Wiring/cables/connectors/	3

2.2.3	Position in snowmobile	4

2.3	Reset / Latching for IMD and BMS	4

2.3.1	Description/circuitry	4

2.3.2	Wiring/cables/connectors	4

2.3.3	Position in snowmobile	4

2.4	Safety System Interlocks	4

2.4.1	Description/circuitry	4

2.4.2	Wiring/cables/connectors	4

2.4.3	Position in snowmobile	4

2.5	Vehicle Energized Light	4

2.5.1	Description/circuitry	4

2.5.2	Wiring/cables/connectors	4

2.5.3	Position in snowmobile	4

2.6	Tractive System Measurement points	5

2.6.1	Description	5

2.6.2	Wiring, connectors, cables	5

2.6.3	Position in snowmobile	5

2.7	Pre-Charge circuitry	5

2.7.1	Description	5

2.7.2	Wiring, cables, current calculations, connectors	5

2.7.3	Position in snowmobile	6

2.8	Discharge circuitry	6

2.8.1	Description	6

2.8.2	Wiring, cables, current calculations, connectors	6

2.8.3	Position in snowmobile	7

2.9	HV Disconnect (HVD)	7

2.9.1	Description	7

2.9.2	Position in snowmobile	7

2.10	Ready-To-Drive-Sound (RTDS)	7

2.10.1	Description	7

2.10.2	Wiring, cables, current calculations, connectors	7

2.10.3	Position in snowmobile	7

3	Battery	8

3.1	Battery pack 1	8

3.1.1	Overview/description/parameters	8

3.1.2	Cell description	8

3.1.3	Cell configuration	9

3.1.4	Cell temperature monitoring	9

3.1.5	Battery management system	9

3.1.6	Accumulator indicator	9

3.1.7	Wiring, cables, current calculations, connectors	9

3.1.8	Battery isolation relays	10

3.1.9	Fusing	11

3.1.10	Charging	11

3.1.11	Mechanical Configuration/materials	12

3.1.12	Position in snowmobile	12

3.2	Battery pack 2	12

4	Motor controller	12

4.1	Motor controller 1	12

4.1.1	Description, type, operation parameters	12

4.1.2	Wiring, cables, current calculations, connectors	13

4.1.3	Position in snowmobile	13

4.2	Motor controller 2	14

5	Motors	14

5.1	Motor 1	14

5.1.1	Description, type, operating parameters	14

5.1.2	Wiring, cables, current calculations, connectors	15

5.1.3	Position in snowmobile	15

5.2	Motor 2	15

6	Torque Control Sensor	16

6.1	Description/additional circuitry	16

6.2	Wiring	16

6.3	Position in snowmobile/mechanical fastening/mechanical connection	16

7	Additional GLV-parts interfering with the tractive system	17

7.1	GLV part 1	17

7.1.1	Description	17

7.1.2	Wiring, cables,	17

7.1.3	Isolation concept	17

7.1.4	Position in snowmobile	17

7.2	GLV part 2	17

8	Firewall(s)	17

8.1	Firewall 1	17

8.1.1	Description/materials	17

8.1.2	Position in snowmobile	17

8.2	Firewall	18

8.3	Other Systems	18

8.3.1	System Description	18

8.3.2	Position in snowmobile	18

9	Appendix	19

# List of Figures

This should be a list of all the figures in the document.  It has to be hyperlinked!

# List of Tables

Table 1.1 General parameters	1

Table 2.1 List of switches in the safety circuit	2

Table 2.2 Wiring – Safety circuit	3

Table 2.3 Parameters of the IMD	3

Table 2.7 General data of the pre-charge resistor	5

Table 2.8 General data of the pre-charge relay	6

Table 2.9 General data of the discharge circuit	7

Table 3.1 Main battery parameters	8

Table 3.2 Main cell specification	9

Table 3.5 Wire data of company A, 20 AWG	10

Table 3.3 Basic BIR data	10

Table 3.4 Basic fuse data	11

Table 3.4Fuse Protection Table	11

Table 3.6 General charger data	12

Table 5.1 General motor controller data	13

Table 6.1 General motor data	14

Table 7.1 Torque control sensor data	16

Has to be hyperlinked!

# List of Abbreviations

# System Overview

- Short description of the system’s concept

- Rough Schematic (blocks) showing all parts affected with the safety and function of the tractive-system

- No detailed wiring

- Additionally fill out the following table, replacing the values with your specifications:

| Maximum Tractive-system voltage: | 300VDC |
| --- | --- |
| Nominal Tractive-system voltage: | 250VDC |
| Grounded Low Voltage-system voltage: | 12VDC, 24VDC |
| Accumulator configuration: | 70s3p |
| Total Accumulator capacity: | 24Ah |
| Motor type: | Permanent magnet synchronous motor |
| Number of motors: | 1 |
| Maximum combined motor power in kW | 150 |

Table 1.1 General parameters

# Safety Systems

## Shutdown Circuit

These sections should cover rules EV5.1.1 and EV5.2

### Description/concept

Describe your concept of the shutdown circuit, the master switches, shut down buttons, tether, etc.

Additionally fill out the following table replacing the values with your specification and append additional switches from your setup:

| Part | Function |
| --- | --- |
| Tractive System Master Switch | Normally open |
| Shutdown buttons | Normally closed |
| Tether | Normally open |
| Insulation Monitoring Device (IMD) | Normally open |
| Battery Management System (BMS) | Normally open |
| Interlocks | Closed when circuits are connected |

Table 2.1 List of switches in the safety circuit

### Wiring / additional circuitry

Describe wiring and additional circuitry, show extra schematics for example if additional transistors etc. are used, also describe the function of additional circuitry and make good use of figures.

Additionally fill out and add information to the following table with respect to the current flowing through the safety circuit:

| Total Number of BIRs: | 10 |
| --- | --- |
| Current per BIR: | 0.5A |
| Additional parts consumption within the safety circuit: | 2A |
| Total current: | 7A |
| Cross sectional area of the wiring used: | 20AWG |

Table 2.2 Wiring – Safety circuit

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the renderings, if necessary.

## IMD

### Description (type, operation parameters)

Describe the IMD used and use a table for the common operation parameters, like supply voltage, temperature, etc. Also describe how the IMD indicator light is wired, etc.  This section should cover rules EV5.3.

Additionally fill out the following table replacing the values with your specification:

| Supply voltage range: | 10..36VDC |
| --- | --- |
| Supply voltage | 24VDC |
| Environmental temperature range: | -40..105°C |
| Selftest interval: | Always at startup, then every 20 minutes |
| High voltage range: | DC 0..1000V |
| Set response value: | 100kΩ (500Ω/Volt) |
| Max. operation current: | 500mA |
| Approximate time to shut down at 50% of the response value: | 27s |

Table 2.3 Parameters of the IMD

### Wiring/cables/connectors/

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.  Be sure to include information on the fusing of the TS leads to the IMD.

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Reset / Latching for IMD and BMS

### Description/circuitry

Describe the concept and circuitry of the latching/reset system for a tripped IMD or BMS.  This section should cover rules EV5.1.5 and EV5.1.7.

### Wiring/cables/connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Safety System Interlocks

### Description/circuitry

Describe the concept and circuitry of the Safety System Interlocks.

### Wiring/cables/connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Vehicle Energized Light

### Description/circuitry

Describe the vehicle energized light and additional circuitry.  This section should cover rules EV4.11.  If a custom PCB is used be sure to show that EV4.1.7 is met.

### Wiring/cables/connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Tractive System Measurement points

### Description

Describe the housing used and how it can be accessed, etc.  This section should cover rules EV4.5.

### Wiring, connectors, cables

Describe wiring, show schematics, and describe connectors, cables and conduit used and show useful data regarding the wiring.

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Pre-Charge circuitry

These sections should cover rules EV4.10.1, EV4.10.2 and EV4.10.3.

### Description

Describe your concept of the pre-charge circuitry.

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

- Give a plot “Percentage of Maximum Voltage” vs. time

- Give a plot Current vs. time

- For each plot, give the basic formula describing the plots

Additionally fill out the tables:

| Resistor Type: | ABC Resistor |
| --- | --- |
| Resistance: | 680Ω |
| Continuous power rating: | 60W |
| Overload power rating: | 200W for 30 sec |
| Voltage rating: | 1500V |
| Cross-sectional area of the wire used: | 20AWG |

Table 2.4 General data of the pre-charge resistor

| Relay Type: | DEF Relay |
| --- | --- |
| Contact arrangment: | SPDT, SPST, SPCO, SPTT, DPST, …. |
| Continuous DC current: | 25A |
| Voltage rating | 2000VDC |
| Cross-sectional area of the wire used: | 0.205 mm² |

Table 2.5 General data of the pre-charge relay

### Position in snowmobile

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

## Discharge circuitry

These sections should cover EV4.10.4 and EV4.10.5.

### Description

Describe your concept of the discharge circuitry.

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

- Give a plot “Voltage” vs. time

- Give the formula describing this behavior

- Give a plot “Discharge current” vs. time

- Give the formula describing your plot

Additionally fill out the table:

| Resistor Type: | ABC Resistor |
| --- | --- |
| Resistance: | 680Ω |
| Continuous power rating: | 350W |
| Overload power rating: | 600W for 20 sec |
| Voltage rating: | 1500V |
| Maximum expected current: | 0.7A |
| Average current: | 0.3A |
| Cross-sectional area of the wire used: | 0.205 mm² |

Table 2.6 General data of the discharge circuit

### Position in snowmobile

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

## HV Disconnect (HVD)

These sections should cover rules EV4.8.

### Description

Describe your concept of the HVD and how it can be operated.  Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors, cables and conduit and show useful data regarding the wiring.

### Position in snowmobile

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

## Ready-To-Drive-Sound (RTDS)

### Description

Describe your concept of the RTDS, how the sound is produced, what are the parameters for activating the RTDS, etc.  This section should cover rules EV4.9 and EV4.12

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables and show useful data regarding the wiring.

### Position in snowmobile

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

# Battery

## Battery pack 1

### Overview/description/parameters

Describe concept of battery pack, provide table with main parameters like number of cells, cell stacks separated by maintenance plugs, cell configuration, resulting voltages->minimum, maximum, nominal, currents, capacity etc.

Fill out the following table:

| Maximum Voltage: | 300VDC |
| --- | --- |
| Nominal Voltage: | 250VDC |
| Minimum Voltage: | 200VDC |
| Maximum output current: | 405A for 10s |
| Maximum nominal current: | 250A |
| Maximum charging current: | 50A |
| Total numbers of cells: | 200 |
| Cell configuration: | 70s3p |
| Total Capacity: | 21.6 MJ |
| Number of cell stacks < 120VDC | 5 |

Table 3.1 Main battery parameters

### Cell description

Describe the cell type used and the chemistry, provide table with main parameters.  This section should cover rule EV3.1.2.

Fill out the following table:

| Cell Manufacturer and Type | Kokam XYZ |
| --- | --- |
| Cell nominal capacity: | 5.4 Ah |
| Maximum Voltage: | 4.2 V |
| Nominal Voltage: | 3.7V |
| Minimum Voltage: | 2.8V |
| Maximum output current: | 20C for 10s |
| Maximum nominal output current: | 15C |
| Maximum charging current: | 5C |
| Maximum Cell Temperature (discharging) | 65°C |
| Maximum Cell Temperature (charging) | 55°C |
| Cell chemistry: | LiFePO4 |

Table 3.2 Main cell specification

### Cell configuration

Describe cell configuration, show schematics, cover additional parts like internal cell fuses etc.  This section should cover rules EV3.3.3, EV3.3.4, EV3.3.5, EV3.3.6 and EV3.3.8.

### Cell temperature monitoring

Describe how the temperature of the cells is monitored, where the temperature sensors are placed, how many cells are monitored, etc. Show schematics, cover additional parts, etc. This section should cover rule EV3.6.5.

### Battery management system

Describe the BMS used, show wiring including fusing / protection for the sense wires, provide tables with operation parameters e.g. at which upper and lower voltage and temperature levels the BMS does react and how, etc.  This section should cover rules EV3.6.  Be sure to include a table of set points for the BMS (over/under voltage, temperature, etc.).  This section should cover any required galvanic isolation in the BMS.

### Accumulator indicator

Describe the indicator, show wiring, provide tables with operation etc.  This section should cover rules EV3.3.10 – EV3.3.12

### Wiring, cables, current calculations, connectors

Describe the internal wiring, show schematics, provide calculations for currents and voltages and show data regarding the cables and connectors used.

- Discuss maximum expected current, DC and AC how long will this be provided?

- Compare the maximum values to nominal currents

- Give a table for each kind of wire in your tractive-system:

- Describe your maintenance plugs, provide pictures

- Use tables like the one shown below:

| Wire type | Company A, |
| --- | --- |
| Continuous current rating: | 150A |
| Wire Gauge | 20 AWG |
| Maximum operating voltage: | 800VDC |
| Temperature rating: | 150 °C |
| Wire connects the following components: | Cell and BMS |

Table 3.3 Wire data of company A, 20 AWG

### Battery isolation relays

Describe the BIRs used and their main operational parameters, use tables, etc.  This section should cover rules EV3.4.13 and EV3.5.

Additionally fill out the following table:

| Relay Type: | ABC Relay |
| --- | --- |
| Contact arragment: | SPST |
| Continous DC current rating: | 100A |
| Overload DC current rating: | 200A for 10sec |
| Maximum operation voltage: | 800VDC |
| Nominal coil voltage: | 24VDC |
| Normal Load switching: | Make and break up to 300A |
| Maximum Load switching | 10 times at 1500A |

Table 3.4 Basic BIR data

### Fusing

Describe the fuses used and their main operational parameters, use tables, etc.

Additionally fill out the following table:

| Fuse type: | MNO Fuse |
| --- | --- |
| Continous current rating: | 150A |
| Maximum operating voltage | 500VDC |
| Type of fuse: | High speed |
| I2t rating: | 1500A2s at 450VDC |

Table 3.5 Basic fuse data

Create a table with components and wires protected by the fuse(s) and the according continuous current rating, below is an example table with some potential entries.  Complete this table with information for your design and add/remove additional locations as applicable.  Ensure that the rating of all of the components is greater than the rating of the fuse such that none of the other components become the fuse.

| Location | Wire Size | Wire Ampacity | Fuse type | Fuse rating |
| --- | --- | --- | --- | --- |
| Cells to BIRs | 2 AWG | XXX | MNO Fuse | XXX |
| BIR to Motor controller | 0 AWG | XXX | 2x MNO Fuse | XXX |
| BIR to Vehicle Energized circuit | 20 AWG | XXX | EFG Fuse | XXX |
| Accumulator output connector | 2 AWG | XXX |  |  |
| Cells to BMS |  |  |  |  |

Table 3.6Fuse Protection Table

### Charging

Describe how the accumulator will be charged. How will the charger be connected? How will the accumulator be supervised during charging? Show schematics, CAD-Renderings, etc., if needed.  This section should cover rules EV8.2.10, EV8.2.11, EV8.2.12 and EV8.2.13.

Additionally fill out the table:

| Charger Type: | ABC Charger |
| --- | --- |
| Maximum charging power: | 3kW |
| Maximum charging voltage: | 550V |
| Maximum charging current: | 20A |
| Interface with accumulator | CAN-Bus, proprietary, serial communication... |
| Input voltage: | 230 VAC |
| Input current: | 16A |

Table 3.7 General charger data

### Mechanical Configuration/materials

Describe the concept of the container, show how the cells are mounted, use CAD-Renderings, show data regarding materials used, etc.  This section should cover EV3.3.1 and EV3.4.

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.  Ensure that the required mechanical structure to protect the accumulator and other electrical components is clearly identified.

## Battery pack 2

…

If identical parts are used, just refer to the corresponding sections, don’t copy and paste.

# Motor controller

## Motor controller 1

### Description, type, operation parameters

Describe important functions, provide table with main parameters like resulting voltages->minimum, maximum, nominal, currents etc.  Describe any required galvanic isolation in the motor controller or how it has been added.

Fill out the following table:

| Motor controller type: | ABC Controller |
| --- | --- |
| Maximum continous power: | 60kW |
| Maximum peak power: | 75kW for 10s |
| Maximum Input voltage: | 600VDC |
| Output voltage: | 250VAC |
| Maximum continuous output current: | 100A |
| Maximum peak current: | 200A for 5s |
| Control method: | PWM, analog signal... |
| Cooling method: | Air, water, oil... |
| Auxiliary supply voltage: | 24VDC |

Table 4.1 General motor controller data

### Wiring, cables, current calculations, connectors

Describe the wiring (including conduit), show schematics, provide calculations for currents and voltages and show data regarding the cables and connectors used.  This section should cover how rules EV4.6 are met for the wiring.

Additionally fill out table:

| Wire type: | Company A, 20AWG |
| --- | --- |
| Current rating: | 150A |
| Maximum operating voltage: | 800V |
| Temperature rating: | 150 °C |

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Motor controller 2

…

If identical parts are used, just refer to the corresponding sections, don’t copy and paste.

# Motors

## Motor 1

### Description, type, operating parameters

Describe the motor used, provide table with main parameters like resulting voltages->minimum, maximum, nominal, currents, resulting motor power, use figures to show important characteristics.

Additionally fill out table:

| Motor Manufacturer and Type: | ABC Motor |
| --- | --- |
| Motor principle | Asynchronous, permanent magnet |
| Maximum continuous power: | 25kW |
| Peak power: | 70kW for 5s |
| Input voltage: | 250VAC |
| Nominal current: | 50A |
| Peak current: | 70A |
| Maximum torque: | 60Nm |
| Nominal torque: | 20Nm |
| Cooling method: | Water, oil, air,... |

Table 5.1 General motor data

- Give a plot of power vs. Rpm including a line for nominal and maximum power

- give a plot of torque vs rpm including a line for nominal and maximum torque

### Wiring, cables, current calculations, connectors

Describe the wiring (including conduit), show schematics, provide calculations for currents and voltages and show data regarding the cables and connectors used.  This section should describe how rules EV4.6 are met for the wiring.

### Position in snowmobile

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary and clearly identify the structure used to protect all relevant parts.

## Motor 2

…

If identical parts are used, just refer to the corresponding sections, don’t copy and paste.

# Torque Control Sensor

## Description/additional circuitry

Describe the type of the torque control sensors used, provide tables with main operation parameters, and describe additional circuitry used to check or manipulate the signal going to the motor controller. Describe how the system reacts if an implausibility or error (e.g. short circuit or open circuit or equivalent) is detected.

This section should address EV2.4.

| Torque encoder manufacturer and type: | ABC Encoder |
| --- | --- |
| Torque encoder principle: | potentiometer |
| Supply voltage: | 5V |
| Maximum supply current: | 20mA |
| Operating temperature: | -20..180 °C |
| Used output: | 0-5V |

Table 6.1 Torque control sensor data

## Wiring

Describe the wiring, show schematics, show data regarding the cables and connectors used.

## Position in snowmobile/mechanical fastening/mechanical connection

Provide CAD-renderings showing all relevant parts and discuss the mechanical actuation. Mark the parts in the rendering, if necessary.

# Additional GLV-parts interfering with the tractive system

## GLV part 1

Describe those parts here which interfere or influence the tractive system, for example a controlling unit that measures track slip and calculates a target torque for the motor or a DC/DC-Converter providing power for the GLV-system from the Tractive-system, etc.

### Description

Describe the parts used and their circuitry, and provide main operation parameters, use tables or figures, etc.

### Wiring, cables,

Describe the wiring, show schematics, etc.

### Isolation concept

Describe your isolation concept here. Discuss how you ensure to satisfy rule EV4.1 and EV4.3.

### Position in snowmobile

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## GLV part 2

…

# Firewall(s)

## Firewall 1

### Description/materials

Describe the concept, layer structure and the materials used for the firewall. Show it meets the requirements of EV3.4.12.

### Position in snowmobile

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

## Firewall

## Other Systems

### System Description

Describe any other powertrain systems on the vehicle that could have safety implications on the operation of the vehicle and the measures that have been taken to ensure that any failure is benign.

### Position in snowmobile

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

# Appendix

Numbering according to chapter 1 to 8

A datasheet for motor controller one for example has to have the numbering 9.4.1

9.2.2 – Bender IR155-3203 IMD ratings

Referred from 2.2.1.

Complete data sheet located at: http://www.bender-de.com/fileadmin/products/doc/IR155-32xx-V004_DB_en.pdf